# Ultra Thin Float Glass for Touch Screens and Displays

Pilkington Microfloat™ and Pilkington Microwhite™ are extremely thin, high-grade float glass products manufactured to precise standards. They are made according to the highest specifications with very low thickness tolerances, to ensure flat and uniform products, suitable for a variety of applications.

The requirements of larger area touch screens and displays are different from those used in mobile devices. Large digital displays do not always require ultra-thin glass, less than 1 mm. Pilkington Microfloat™ and Pilkington Microwhite™ are both manufactured by the standard float glass process. Pilkington Microfloat™ is the classic version manufactured from clear float, the new Pilkington Microwhite™ is a low iron composition which produces a very pure, clear glass and has the added benefit of increased light transmission.

Both Pilkington Microfloat™ and Pilkington Microwhite™ are ideal for a wide range of uses, including the production of microscope slides, cosmetic mirrors, chromatographic plates, LCD photo masks, automotive and technical glass, PC display screens and tablet PC’s.

Various available glass thicknesses are suitable for microscope slides (0,95-1,05 mm), microscope slides and cosmetic mirrors (1,0-1,2 mm), chromatographic plates, cosmetic mirrors and technical glass (1,2-1,4 mm) and photomasks, automotive and technical glass (1,5-1,7 mm).

These high performance glass products will be displayed at the NSG Group booth #8-D352.

For more information please visit: http://www.pilkington.com/en/digital-signage

ENDS

Note to editors:

The NSG Group is one of the world's leading manufacturers of glass and glazing systems in three major business areas: Automotive, Architectural and Technical Glass. Automotive serves the original equipment, aftermarket replacement, and specialized transport glazing markets. Architectural supplies glass for architectural and solar energy applications. Technical Glass products include very thin glass for displays, lenses and light guides for printers, and glass fiber, used in battery separators and engine timing belts. We have major market shares in most building and automotive product markets of the world, with a broad geographic reach, enabling us to respond to customers whose operations, particularly in the case of Automotive OE, are increasingly global. Geographically, 39 percent of the Group's sales are in Europe, 30 percent in Japan and 16 percent in North America, with the remaining 15 percent being generated in the rest of the world.

# Text boxes

January 30, 2015

PRESS RELEASE