# NBS L40 Guidance Notes for Pilkington Suncool™ High Performance Solar Control with Low-E Thermal Insulation

# from Pilkington United Kingdom Limited

# Product:

Pilkington Suncool™ 60/31 Pro T

Processing Options:

Toughened, Heat Strengthened, Laminated*

### Thickness:

6, 8, 10 and 12 mm

* Laminated option can be a heat strengthened or

toughened combination of the above thicknesses.

NOTE: 	For project specific glass thickness and composition please contact– Enquires@Pilkington.com

L40	GENERAL GLAZING

To be read with Preliminaries/ General conditions.

GENERAL REQUIREMENTS

L40/111	PREGLAZING

-	Preglazing of components: Permitted.

-	Prevention of displacement: Submit details of precautions to be taken to protect glazing and compound/ seals during delivery and installation.

-	Defective/ displaced glazing/ compound/ seals: Reglaze components in situ.

L40/150	WORKMANSHIP GENERALLY

-	Glazing generally: To BS 6262.

-	Integrity: Glazing must be wind and watertight under all conditions with full allowance made for deflections and other movements.

-	Dimensional tolerances: Panes/ sheets to be within ± 3 mm of specified dimensions.

-	Materials:

-	Compatibility: Glass/ plastics, surround materials, sealers, primers and paints/ clear finishes to be used together to be compatible. Avoid contact between glazing panes/ units and alkaline materials such as cement and lime.

-	Protection: Keep materials dry until fixed. Protect insulating glass units and plastics glazing sheets from the sun and other heat sources.

L40/152	PREPARATION

-	Surrounds, rebates, grooves and beads: Clean and prepare before installing glazing.

L40/155	GLASS GENERALLY

-	Standards: To BS 952 and relevant parts of:

-	BS EN 572 for basic soda lime silicate glass.

-	BS EN 1096 for coated glass.

-	BS EN 1748-1-1 for borosilicate glass.

-	BS EN 1748-2-1 for ceramic glass.

-	BS EN 1863 for heat strengthened soda lime silicate glass.

-	BS EN 12150 for thermally toughened soda lime silicate safety glass.

-	BS EN 12337 for chemically strengthened soda lime silicate glass.

-	BS EN 13024 for thermally toughened borosilicate safety glass.

-	BS EN ISO 12543 for laminated glass and laminated safety glass.

-	Panes/ sheets: Clean and free from obvious scratches, bubbles, cracks, rippling, dimples and other defects.

-	Edges: Generally undamaged. Shells and chips not more than 2 mm deep and extending not more than 5 mm across the surface are acceptable if ground out.

L40/165	HEAT SOAKING OF THERMALLY TOUGHENED GLASS

-	Standard: To BS EN 14179.

-	Holding period (minimum): 2 hours

-	Mean glass temperature: 290° ±10°C.

-	Certified evidence of treatment: Submit.

-	Designated locations: By others

TYPES OF GLAZING

L40/370	INSULATING GLASS UNITS

-	Glazing units to be manufactured in accordance with EN1279

-      Option for Pilkington Optiwhite™ (OW) low iron substrate for visual clarity can be specified.

L40/370A	INSULATING GLASS UNITS

-	Manufacturer: Pilkington United Kingdom Limited

Contact: Jason.Eggerton@NSG.com (UK Specification Sales Manager)

Mobile: 07817 200350

NOTE: For Project specific glass thickness and composition please contact above.

Pilkington Suncool™ IGU Manufacturing Partners: https://www.pilkington.com/en-gb/uk/products/product-categories/solar-control/pilkington-suncool-range/pilkington-suncool-partners

-	Pane material:

-	Outer pane: 	6mm Pilkington Suncool™ 60/31 Pro T

-	Inner pane: 	6mm Pilkington Optifloat™ or 8.8mm Pilkington Optilam™

-	Cavity: 		16mm Spacer (90% argon gas filled cavity)

-	Perimeter taping: 	Do not use.

Processing:	Pro T and Float is Toughened (T) and Heat Soak Tested (HST)

Pilkington Optilam™ is annealed with all edges ground (subject to thermal safety check)

-              Light:

Minimum Light Transmission (LT)	60%

External Light Reflectance (LR out)	11%

Internal Light Reflectance (LR in)	18%

Energy:

Direct Transmittance (ET)		29%

Reflectance (ER)			32%

Absorptance (EA)			38%

Total Transmittance (g)		0.32

Shading Coefficient Total		0.37

Shading Coefficient Shortwave	0.34

Thermal:

U value (W/m2K)			1.0

-	Glazing system: TBC .

-	Glazing installation:

-	Insulating unit: Located centrally in surround using setting and location blocks.

-	Gaskets and beads: Installed as recommended by frame manufacturer.

-	Gasket fit at corners: Tight, without gaps.

-	Drainage and ventilation holes: Unobstructed.